Annex 1

Data elements and format

Header refers to items that should have a single value established at trigger or before the event.  Data in pre-trigger shall be reported at least 2 values per second for at least 5 seconds before a trigger.

Table 1 - List of data elements

| Data element | Condition for requirement | Recording interval/time (relative to time zero trigger event) | Data sample rate (samples per second) | Minimum range | Accuracy | Resolution | Data recorded for the following triggers |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Event Data Recording Complete | Mandatory | [Following other data] | N/A | Yes or No | N/A | Yes or No | All 3.3.1 triggers Planar VRU Rollover |
| Event Data Recording Complete | Mandatory | [Following other data] | [N/A] | [Yes or No] | [N/A] | [Yes or No] | All 3.3.1 triggers Planar VRU Rollover |
| [Engine hours event] | Mandatory | [-1.0 sec] | [N/A] | [0 to 210,554,060.75 hr] | [±0.05 hr] | [0.05 hr] | All 3.3.1 triggers |
| [Engine hours download] | Mandatory | [At time of download] | [N/A] | [0 to 210,554,060.75 hr] | [±0.05 hr] | [0.05 hr] | All 3.3.1 triggers |
| [Odometer] |  |  |  |  |  |  | All 3.3.1 triggers |
| Odometer |  |  |  |  |  |  | All 3.3.1 triggers |
| HD EDR Unit Hardware Part # | Mandatory | N/A | N/A | N/A | N/A | N/A | N/A |
| HD EDR Unit Software Part # | Mandatory | N/A | N/A | N/A | N/A | N/A | N/A |
| Vehicle Make | Mandatory | [Event] | [N/A] | [N/A] | [N/A] | [Alphanumeric type-variant-version code] | All 3.3.1 triggers |
| Vehicle Make | Mandatory |  |  |  |  |  |  |
| Vehicle Model | Mandatory |  |  |  |  |  | All 3.3.1 triggers |
| Vehicle Model | Mandatory |  |  |  |  |  | All 3.3.1 triggers |
| [Conversion factor between drive shaft rpm and vehicle speed] |  |  |  |  |  |  | All 3.3.1 triggers |
| [Conversion factor between drive shaft rpm and vehicle speed] |  |  |  |  |  |  | All 3.3.1 triggers |
| Trigger Thresholds | Mandatory | [Event] | [N/A] | [8.0 to 22.5 km/h/s] | [N/A] | [0.1 km/h/s] | All 3.3.1 triggers |
| Trigger Threshold Activated | Mandatory | [Event] | [N/A] | [N/A] | [N/A] | [Deceleration, Last stop, AEB, ABS, Safety restraint system, VRU secondary safety system, Other] | All 3.3.1 triggers |
| Vehicle configuration [pending more info from SAE expert] |  |  |  |  |  |  | All 3.3.1 triggers |
| Vehicle configuration [pending more info from SAE expert] |  |  |  |  |  |  | All 3.3.1 triggers |
| [Vehicle Safety System Manifest] | [Mandatory] | [Event] | [N/A] | [N/A] | [N/A] | [List of fitted active safety and accident avoidance systems] | All 3.3.1 triggers |
| [Vehicle Safety System Manifest] |  |  |  |  |  |  | All 3.3.1 triggers |
| [Ignition cycle crash] | [Mandatory] | [-1.0 sec] | [N/A] | [0 to 60,000] | [±1 cycle] | [1 cycle] | All 3.3.1 triggers |
| [Ignition cycle download] | [Mandatory] | [At time of download] | [N/A] | [0 to 60,000] | [±1 cycle] | [1 cycle] | All 3.3.1 triggers |
| Vehicle Speed | Mandatory | [-5.0 to 0 sec -20 to +10 sec] | [2 10] | [0 to 250 km/h] | [±1 km/h] | [1 km/h] | All 3.3.1 triggers |
| Vehicle Speed | Mandatory | [-5.0 to 0 sec] | [2] | [0 to 250 km/h] | [±1 km/h] | [1 km/h] | All 3.3.1 triggers Planar VRU |
| Retarder Torque Mode | Mandatory |  |  |  |  |  | All 3.3.1 triggers |
| Retarder Torque Mode | Mandatory | -5.0 to 0 sec | 2 | NA | NA | NA | All 3.3.1 triggers |
| Brake Status – Parking | Mandatory | [-5.0 to 0 sec] | [2] | [On or Off] | [NA] | [On or Off] | All 3.3.1 triggers |
| Brake Status – Parking | Mandatory | [-5.0 to 0 sec -20 to +10 sec] | [2 10] | [On or Off N/A] | [NA] | [On or Off] | All 3.3.1 triggers |
| Brake Status – Service | Mandatory | [-5.0 to 0 sec -20 to +10 sec] | [2 10] | [On or Off N/A] | [NA] | [On or Off] | All 3.3.1 triggers Planar VRU Rollover |
| Brake Status – Service | Mandatory | [-5.0 to 0 sec] | [2] | [On or Off] | [NA] | [On or Off] | Planar VRU Rollover All 3.3.1 triggers |
| Engine Speed | Mandatory | [-5.0 to 0 sec -20 to +10 sec] | [2 10] | [0-10,000 rpm] | [±100 rpm] | [100 rpm][ | All 3.3.1 triggers Planar Rollover |
| Engine Speed | Mandatory | [-5.0 to 0 sec] | [2] | [0-10,000 8,031 rpm] | [±100 rpm] | [100 rpm][ | All 3.3.1 triggers Planar Rollover |
| Engine Load | Mandatory | [-5.0 to 0 sec -20 to +10 sec] | [2 10] | [0 to 125%] | [±5%] | [1%] | All 3.3.1 triggers |
| Engine Load | Mandatory | -5.0 to 0 sec | 2 | -125 – 125 % | ±5% | 1% | All 3.3.1 triggers |
| Accelerator Pedal Position | Mandatory | [-5.0 to 0 sec -20 to +10 sec] | [2 10] | [0 to 100 %] | [±5%] | [1%] | All 3.3.1 triggers Planar Rollover VRU |
| Accelerator Pedal Position | Mandatory | [-5.0 to 0 sec] | [2] | [0 to 100 %] | [±5%] | [1%] | All 3.3.1 triggers Planar Rollover VRU |
| ABS Brake Control Status – Tractor/Truck Motor vehicle | Mandatory | [-5.0 to 0 sec -20 to +10 sec] | [2 10] | [Faulted, Non-Engaged, Engaged N/A] | [NA] | [Faulted, Non-Engaged, Engaged Off, Faulted, On not intervening, On intervening] | All 3.3.1 triggers Planar VRU Rollover |
| ABS Brake Control Status – Tractor/Truck | Mandatory | [-5.0 to 0 sec] | [2] | [Faulted, Non-Engaged, Engaged] | [NA] | [Faulted, Non-Engaged, Engaged] | All 3.3.1 triggers Planar VRU Rollover |
| ABS Brake Control Status – Trailer | Mandatory | [-5.0 to 0 sec -20 to +10 sec] | [2 10] | [Faulted, Non-Engaged, Engaged N/A] | [NA] | [Faulted, Non-Engaged, Engaged Off, Faulted, On not intervening, On intervening] | All 3.3.1 triggers Planar VRU Rollover |
| ABS Brake Control Status – Trailer | Mandatory | [-5.0 to 0 sec] | [2] | [Faulted, Non-Engaged, Engaged] | [NA] | [Faulted, Non-Engaged, Engaged] | All 3.3.1 triggers Planar VRU Rollover |
| Adaptive Cruise Control Mode | Mandatory | [-5.0 to 0 second relative to time zero] | [2] | [NA Off (Standby, enabled, ready for activation) Speed control active Distance control active] | [NA] | [Engaged, Faulted, Off, Non-Engaged Off Speed control active Distance control active] | All 3.3.1 triggers Planar VRU Rollover |
| ACC Mode | Mandatory | [-5.0 to 0 second relative to time zero -20 to +10 sec] | [2 10] | [NA] | [NA] | [Engaged, Faulted, Off, Non-Engaged Off, Faulted, On not controlling, On controlling] | All 3.3.1 triggers Planar VRU Rollover |
| ACC Set Distance |  |  |  |  |  |  | All 3.3.1 triggers |
| Cruise Control States | Mandatory | [-5.0 to 0 second -20 to +10 sec] | [2 10] | [NA] | [NA] | [Engaged, Faulted, Off, Non-Engaged Off, Faulted, On not controlling, On controlling] | All 3.3.1 triggers Planar VRU Rollover |
| Cruise Control States | Mandatory | [-5.0 to 0 second ] | [2] | [NA Off/Disabled Hold Accelerate Decelerate Resume Set Accelerator Override Faulted] | [NA] | [Engaged, Faulted, Off, Non-Engaged Same as range] | All 3.3.1 triggers Planar VRU Rollover |
| Automatic Emergency Braking | Mandatory | [-5.0 to 0 second relative to time zero -20 to +10 sec] | [2 10] | [N/A] | [N/A] | [Faulted, Deactivated, On but Non-Engaged, Engaged Off, Faulted, On not warning/intervening, On warning, On intervening] | All 3.3.1 triggers Planar VRU Rollover |
| Automatic Emergency Braking | Mandatory | [-5.0 to 0 second relative to time zero] | [2] | [N/A system is not ready system is temporarily not available system is deactivated by driver system is ready and activated driver overrides system forward collision warning active forward collision warning with braking forward collision emergency braking active] | [N/A] | [Faulted, Deactivated, On but Non-Engaged, Engaged Same as range] | All 3.3.1 triggers Planar VRU Rollover |
| Time to Collision with Relevant Object [not required] |  |  |  |  |  |  |  |
| Speed of Forward vehicle [not required] |  |  |  |  |  |  |  |
| Distance to forward vehicle [not required] |  |  |  |  |  |  |  |
| Lane Departure Warning System State Status | Mandatory | [-5.0 to 0 sec -20 to +10 sec] | [2 10] | [N/A] | [N/A] | [Faulted, Off, On but not warning, On – Warning left, On – Warning right] | All 3.3.1 triggers Planar Rollover |
| Lane Departure Warning System State | Mandatory | [-5.0 to 0 sec] | [2] | [N/A Active - Inactive] | [N/A] | [Faulted, Off, On but not warning, On – Warning left, On – Warning right Active - Inactive] | All 3.3.1 triggers Planar Rollover |
| Steering wheel angle | Mandatory | [-5.0 to 0 sec -20 to +10 sec] | [2 10] | [-250 deg CW to + 250 deg CCW] | [±5%] | [±1%] | All 3.3.1 triggers Planar VRU Rollover |
| Steering wheel angle | Mandatory | [-5.0 to 0 sec] | [2] | [-250 deg CW to + 250 deg CCW -31 to 31 rad] | [±5% ±0.4 rad] | [±1% 0.2 rad] | All 3.3.1 triggers [Planar VRU Rollover |
| Rollover Protection Engine Control | Mandatory | [-20 to +10 sec] | [10] | [N/A] | [N/A] | [Off, Faulted, On not intervening, On intervening] | All 3.3.1 triggers |
| Stability Control System Braking [Rollover protection Engine Control] | Mandatory | [-20 to +10 sec] | [10] | [N/A] | [N/A] | [Off, Faulted, On not intervening, On intervening] | All 3.3.1 triggers |
| Stability Control System Braking | Mandatory | -5.0 to 0 sec | 2 | Active – Inactive (foundation braking) | NA | Active - Inactive | All 3.3.1 triggers |
| Yaw Control Engine Retarder Control | Mandatory | [-20 to +10 sec] | [10] | [N/A] | [N/A] | [Off, Faulted, On not intervening, On intervening] | All 3.3.1 triggers |
| Yaw Control Brakinge Control | Mandatory | [-20 to +10 sec] | [10] | [N/A] | [N/A] | [Off, Faulted, On not intervening, On intervening] | All 3.3.1 triggers |
| Vehicle Dynamic Control System State | Mandatory |  |  |  |  |  | All 3.3.1 triggers |
| Vehicle Dynamic Control System State Stability Control System State | Mandatory | -5.0 to 0 sec | 2 | Active - Inactive | NA | Active - Inactive | All 3.3.1 triggers |
| Blind Spot Warning System Status (Vehicle detection) | Mandatory | [-20 to +10 sec] | [10] | [N/A] | [N/A] | [Faulted, Off, On not warning, On warning left, On warning right] | All 3.3.1 triggers |
| Blind Spot Warning System Status | Mandatory | -5.0 to 0 sec | 2 | Active - Inactive | NA | Active - Inactive | All 3.3.1 triggers |
| Crash Type [Impact Mitigation] System Activation Notification | Mandatory | Event | N/A | N/A | N/A | Frontal crash, Rear crash, Side crash (left), Side crash (right), Rollover | All 3.3.1 triggers |
| Safety Seat Belt Status (Driver) | Mandatory | [-1.0 sec] | [N/A] | [Fastened, not Fastened N/A] | [N/A] | [Fastened, not Fastened] | [All 3.3.1 triggers] |
| Seat Belt Status (Driver) | Mandatory | [-1.0 sec] | [N/A] | [Fastened, not Fastened] | [N/A] | [Fastened, not Fastened] | [All 3.3.1 triggers] |
| Safety Seat Belt Status (Passenger) | Mandatory | [-1.0 sec] | [N/A] | [Fastened, not Fastened N/A] | [N/A] | [Fastened, not Fastened] | [All 3.3.1 triggers] |
| Seat Belt Status (Front Outboard Passenger) | Mandatory | [-1.0 sec] | [N/A] | [Fastened, not Fastened] | [N/A] | [Fastened, not Fastened] | [All 3.3.1 triggers] |
| Safety Restraint System Status | Mandatory | [Event] | [N/A] | [N/A] | [N/A] | [Record for each pre-tensioner and airbag separately: Off, Faulted, Deployed] | All 3.3.1 triggers |
| Safety Restraint System Status | Mandatory | -5.0 to 0 sec | 2 | Active - Inactive | NA | Active - Inactive | All 3.3.1 triggers |
| VRU Alert Secondary Safety System Status | Mandatory | [-1.1 to 0 relative to time zero Event] | [N/A] | [N/A] | [N/A] | [On or Off Faulted, Deployed] | All 3.3.1 triggers VRU |
| VRU Alert | Mandatory | [-1.1 to 0 relative to time zero -5.0 to 0 sec] | [N/A 2] | [N/A Active, Inactive] | [N/A] | [On or Off Active, Inactive] | All 3.3.1 triggers VRU |
| VRU Alert - Left Side | Mandatory | [-20 to +10 sec] | [10] | [N/A] | [N/A] | [Off, Faulted, On not informing/warning/intervening, On informing, On warning, On intervening] | All 3.3.1 triggers |
| VRU Alert - Right Side | Mandatory | [-20 to +10 sec] | [10] | [N/A] | [N/A] | [Off, Faulted, On not informing/warning/intervening, On informing, On warning, On intervening] | All 3.3.1 triggers |
| VRU Alert - Front | Mandatory | [-20 to +10 sec] | [10] | [N/A] | [N/A] | [Off, Faulted, On not informing/warning/intervening, On informing, On warning, On intervening] | All 3.3.1 triggers |
| VRU Alert - Rear | Mandatory | [-20 to +10 sec] | [10] | [N/A] | [N/A] | [Off, Faulted, On not informing/warning/intervening, On informing, On warning, On intervening] | All 3.3.1 triggers |
| [Delta-V, longitudinal] | [Mandatory - not required if longitudinal acceleration recorded at ≥500 Hz with sufficient range and resolution to calculate delta-v with required accuracy] | [0 to 250 ms or 0 to End of Event Time plus 30 ms, whichever is shorter.] | [100] | [-100 km/h to + 100 km/h.] | [±10%] | [1 km/h.] | [Planar] |
| [Maximum delta-V, longitudinal] | [Mandatory - not required if longitudinal acceleration recorded at ≥500 Hz] | [0–300 ms or 0 to End of Event Time plus 30 ms, whichever is shorter.] | [N/A] | [-100 km/h to + 100 km/h.] | [±10%] | [1 km/h.] | Occupant restraint system (planar events) |
| [Maximum delta-V, longitudinal] | [Mandatory - not required if longitudinal acceleration recorded at ≥500 Hz] | [0–300 ms or 0 to End of Event Time plus 30 ms, whichever is shorter.] | [N/A] | [-100 km/h to + 100 km/h.] | [±10%] | [1 km/h.] | Occupant restraint system (planar events) Planar |
| [Time, maximum delta-V, longitudinal] | [Mandatory - not required if longitudinal acceleration recorded at ≥500 Hz] | [0–300 ms or 0 to End of Event Time plus 30 ms, whichever is shorter.] | [N/A] | [0–300 ms, or 0-End of Event Time plus 30 ms, whichever is shorter.] | [±3 ms] | [2.5 ms.] | Occupant restraint system (planar events) |
| [Time, maximum delta-V, longitudinal] | [Mandatory - not required if longitudinal acceleration recorded at ≥500 Hz] | [0–300 ms or 0 to End of Event Time plus 30 ms, whichever is shorter.] | [N/A] | [0–300 ms, or 0-End of Event Time plus 30 ms, whichever is shorter.] | [±3 ms] | [2.5 ms.] | Occupant restraint system (planar events) Planar |
| [Delta-V lateral] | [Mandatory - not required if longitudinal acceleration recorded at ≥500 Hz with sufficient range and resolution to calculate delta-v with required accuracy] | [0 to 250 ms or 0 to End of Event Time plus 30 ms, whichever is shorter.] | [100] | [-100 km/h to + 100 km/h.] | [±10%] | [1 km/h.] | [Planar] |
| [Maximum delta-V, lateral] | [Mandatory - not required if lateral acceleration recorded at ≥500 Hz ] | [0–300 ms or 0 to End of Event Time plus 30 ms, whichever is shorter.] | [N/A] | [-100 km/h to + 100 km/h.] | [±10%] | [1 km/h.] | Occupant restraint system (Planer events) |
| [Time, maximum delta-V, lateral] | [Mandatory - not required if lateral acceleration recorded at ≥500 Hz] | [0–300 ms or 0 to End of Event Time plus 30 ms, whichever is shorter.] | [N/A] | [0–300 ms, or 0-End of Event Time plus 30 ms, whichever is shorter.] | [±3 ms] | [2.5 ms.] | Occupant restraint system (planar events) |
| [Time for maximum delta-V, resultant] | [Mandatory - not required if lateral acceleration recorded at ≥500 Hz] | [0–300 ms or 0 to End of Event Time plus 30 ms, whichever is shorter.] | [N/A] | [0–300 ms, or 0-End of Event Time plus 30 ms, whichever is shorter.] | [±3 ms] | [2.5 ms.] | Occupant restraint system (planar events |
| [Time for maximum delta-V, resultant] | [Mandatory - not required if relevant acceleration recorded at ≥500 Hz] | [0–300 ms or 0 to End of Event Time plus 30 ms, whichever is shorter.] | [N/A] | [0–300 ms, or 0-End of Event Time plus 30 ms, whichever is shorter.] | [±3 ms] | [2.5 ms.] | Occupant restraint system (planar events) |
| [Roll angle] | [If recorded] | [0 to at least 250ms -20 to +10 sec] | [10] | [-1080 deg to + 1080 deg.] | [±10%] | [10 deg.] | Occupant restraint system (rollover events) |
| [Roll rate] | [Mandatory if fitted and used for rollover protection system control algorithm] | [0 to at least 250ms -20 to +10 sec] | [10] | [-240 to +240 deg/sec] | [±10%] | [4 deg/sec] | Occupant restraint system (rollover events) |
| [Longitudinal Acceleration (pre-crash low frequency)] | [Mandatory] | [-5.0 to 0 second relative to time zero -20 to +10 sec] | [2 10] | [-1.5g to +1.5g] | [±10%] | [0.1g] | All 3.3.1 triggers |
| [Lateral Acceleration (pre-crash low frequency)] | [Mandatory] | [-5.0 to 0 second relative to time zero -20 to +10 sec] | [2 10] | [-1.5g to +1.5g] | [±10%] | [0.1g] | All 3.3.1 triggers |
| [Longitudinal Acceleration (pre-crash] | [Mandatory] | [-5.0 to 0 second relative to time zero] | [2] | [-1.5g to +1.5g] | [±10%] | [0.1g] | All 3.3.1 triggers Planar VRU |
| [Lateral Acceleration (pre-crash | [Mandatory] | [-5.0 to 0 second relative to time zero] | [2] | [-1.5g to +1.5g] | [±10%] | [0.1g] | All 3.3.1 triggers Planar VRU |
| Accident emergency call system status | Mandatory | [Event] | [N/A] | [N/A] | [N/A] | [Faulted, On but emergency call not automatically triggered, On – Emergency call automatically triggered] | Occupant restraint system |
| Tyre pressure monitoring system warning lamp status | Mandatory | [-1.0 second relative to time zero] | [N/A] | [N/A] | [N/A] | [On, Off] | All 3.3.1 triggers |
| [Safety belt status, rear passengers] | [Mandatory] | [-1.0 sec] | [N/A] | [Fastened, not Fastened N/A] | [N/A] | [Fastened, not Fastened [Number of fastened rear passenger safety belts and number of occupied rear passenger seats] | All 3.3.1 triggers |
| [Safety belt status mid-position front] | [Mandatory] | [-1.0 sec] | [N/A] | [Fastened, not Fastened N/A] | [N/A] | [Fastened, not Fastened] | All 3.3.1 triggers Planar Rollover |
| [Moving Off Information System Status (M2, 3 and N2, 3)] |  |  |  |  |  |  | All 3.3.1 triggers |
| [VRU Proximity Sensing system reversing motion status (M2, 3, and N2,3)] |  |  |  |  |  |  | All 3.3.1 triggers |
| [Yaw Rate] | [Mandatory] | [-5 to 0 seconds relative to time zero -20 to +10 sec] | [2 10] | [-75 to +75 degrees/second] | [±10% of the full range of the sensor] | [0.1 ???] | Occupant restraint system (planar events) Planar Rollover |
| [Corrective steering function status] | [Mandatory] | [-5 to 0 seconds relative to time zero -20 to +10 sec] | [2 10] | N/A | N/A | [Faulted, Off, On but not engaged, engaged [intervening, On intervening] | All 3.3.1 triggers Planar Rollover |
| [Emergency steering function status] | [Mandatory] | [-5 to 0 seconds relative to time zero -20 to +10 sec] | [2 10] | [N/A] | [N/A] | [Faulted, Off, On but not engaged, engaged [controlling, On controlling] | All 3.3.1 triggers Planar Rollover |
| [Automatically commanded steering function category A status] | [Mandatory] | [-5 to 0 seconds relative to time zero -20 to +10 sec] | [2 10] | [N/A] | [N/A] | [Faulted, Off, On but not engaged, engaged [controlling, On controlling] | All 3.3.1 triggers Planar Rollover |
| [Automatically commanded steering function category B status] | [Mandatory] | [-5 to 0 seconds relative to time zero -20 to +10 sec] | [2 10] | [N/A] | [N/A] | [Faulted, Off, On but not engaged, engaged [controlling, On controlling] | All 3.3.1 triggers Planar Rollover |
| [Automatically commanded steering function category C status] | [Mandatory] | [-5 to 0 seconds relative to time zero -20 to +10 sec] | [2 10] | [N/A] | [N/A] | [Faulted, Off, On but not engaged, engaged [controlling, On controlling] | All 3.3.1 triggers Planar Rollover |
| [Automatically commanded steering function category D status] | [Mandatory] | [-5 to 0 seconds relative to time zero -20 to +10 sec] | [2 10] | [N/A] | [N/A] | [Faulted, Off, On but not engaged, engaged [controlling, On controlling] | All 3.3.1 triggers Planar Rollover |
| [Automatically commanded steering function category E status] | [Mandatory] | [-5 to 0 seconds relative to time zero -20 to +10 sec] | [2 10] | [N/A] | [N/A] | [Faulted, Off, On but not engaged, engaged [controlling, On controlling] | All 3.3.1 triggers Planar Rollover |

| Data Element | Description |
| --- | --- |
| [Event Data Recording Complete] | [This data indicates whether a complete set of data that the event data recording device is designed to capture was successfully recorded by and stored in the device.] |
| Event Date [exclude from scope] | The date when the event occurred |
| [Engine Hours] | The number of hours that the engine has been operating from the time of control unit first use to the time of the event trigger |
| [Odometer] | Total vehicle distance at the time of the event trigger |
| Latitude [exclude from scope] | Vehicle position per GNSS at the time of the event |
| Longitude [exclude from scope] | Vehicle position per GNSS at the time of the event |
| Event Time [exclude from scope] | The time when the event occurred |
| HD EDR Unit Hardware Part # | The part number for the HD EDR unit |
| HD EDR Unit Software Part # | The part number/software version number for the HD EDR software |
| Vehicle Make | The name of the vehicle manufacturer |
| Vehicle Model | The vehicle’s model name/number |
| Rear Axle Ratio [pending more info from SAE expert] | Ratio of transmission output shaft speed to tire rotation rate |
| Tire Size [pending more info from SAE expert] | Tire size in revolutions per km |
| Trigger Thresholds | Lists the currently configured trigger threshold(s). |
| Trigger Threshold Activated | Indicates which Trigger Threshold was activated to cause the recording the event. |
| Vehicle Configuration[pending more info from SAE expert] | PGN 65259 and PGN 65242 for available ECU HW and SW part number (needs further clarification from SAE expert) |
| [Vehicle Safety System Manifest] | Manifest of key vehicle safety systems fitted to the vehicle |
| [Ignition cycle, crash] | The number (count) of power mode cycles at the time when the crash event occurred since the first use of the EDR. |
| [Ignition cycle, download] | The number (count) power mode cycles at the time when the data was downloaded since the first use of the EDR. |
| Vehicle Speed | The longitudinal speed of the vehicle that is calculated or estimated from the vehicle speed sensor (VSS). |
| Retarder Torque Mode | State signal which indicates which retarder torque mode is currently generating, limiting, or controlling retarder torque. |
| Brake Status – Parking | Indicates the status of the switch that is installed to detect whether or not the parking brake has been applied. |
| Brake Status – Service | Indicates the status of the switch that is installed in brake system to detect whether the service brake has been applied. This switch is usually used to turn on the brake lamps. |
| Engine Speed | Rotational speed of the engine output shaft. |
| Engine Load | Percent of available engine torque being generated |
| Accelerator Pedal Position | Ratio of the throttle pedal opening (driver’s operation) in percent. |
| ABS Brake Control Status – Tractor | Indicates the status of the ABS Brake control system on the vehicle/tractor, active or not active. |
| ABS Brake Control Status – Trailer | Indicates the status of the ABS Brake control system on Trailer(s), active or not active. Active if ABS Brake control is active for any trailer. |
| ACC Mode | Control status of Adaptive Cruise Control |
| Cruise Control States | The current state, or mode, of operation by the cruise control device |
| Automatic Emergency Braking | Forward Collision Advanced Emergency Braking System state |
| Time to Collision with Relevant Object [not required] | The time to collision is the duration after which the predicted travelling paths of host vehicle and relevant object lead to a distance of 0m between both. |
| Speed of Forward Vehicle [not required] | Absolute velocity of the preceding vehicle situated within 250 m in the same lane and moving in the same direction |
| Distance to Forward Vehicle [not required] | Distance to the preceding vehicle situated within 250 m in the same lane and moving in the same direction. |
| Lane Departure Warning System State | Indicates the status of Lane Departure Warning system. |
| Steering wheel angle | Angle of the steering shaft connected to driver control |
| Rollover Protection Engine Control | Stability control of engine retarder for rollover protection |
| Stability Control Braking [only on foundation brake application/control] | Stability control of wheel brakes for Roll Over Protection or Yaw Control |
| Yaw Control of Engine Retarder | Stability control of engine retarder for yaw control |
| Yaw Control of Wheel Brakes | Stability control of wheel brakes for yaw control |
| VDC System State | VDC Operational State (Can this be combined into a single signal with stability control above?) |
| Blind Spot Warning System Status | Operating status of the blind spot warning system |
| Crash [Impact Mitigation] System Activation Notification | Indicates detection and type of crash by installed crash mitigation system. |
| Seat Belt Status (Driver) | Shows if buckled or not |
| Seat Belt Status (Passenger) | Shows if buckled or not |
| Safety Restraint System Status | Operating status of safety restraint system(s) |
| [Delta-V, longitudinal] | The cumulative change in velocity, as recorded by the EDR of the vehicle, along the longitudinal axis. |
| [Maximum delta-V, longitudinal] | The maximum value of the cumulative change in velocity, as recorded by the EDR, of the vehicle along the longitudinal axis. |
| [Time, maximum delta-V, longitudinal] | The time from crash time zero to the point where the maximum value of the cumulative change in velocity is found, as recorded by the EDR, along the longitudinal axis. |
| [Maximum delta-V, lateral] | The maximum value of the cumulative change in velocity, as recorded by the EDR, of the vehicle along the lateral axis. |
| [Time, maximum delta-V, lateral] | The time from crash time zero to the point where the maximum value of the cumulative change in velocity is found, as recorded by the EDR, along the lateral axis. |
| [Maximum delta-V, resultant] | The maximum value of the cumulative change in velocity, as recorded by the EDR, of the vehicle along the lateral and longitudinal axis. |
| [Time, maximum delta-V, resultant] | The time from crash time zero to the point where the maximum value of the cumulative change in velocity is found, as recorded by the EDR, along the lateral and longitudinal axis. |
| [Roll angle] |  |
| [Roll rate] |  |
| [Pre-crash acceleration, longitudinal] | 10Hz |
| [Pre-crash acceleration, lateral] | 10Hz |
| Accident Emergency Call System Status | Operating status of emergency call system |
| VRU System Status | Operating status of the VRU system |
| Tyre Pressure Monitoring System Status | Operating status of the tire Pressure Monitoring System |

# Footnotes

Format requirements specified below are minimum requirements and manufacturers can exceed them.

"Mandatory" is subject to the conditions detailed in Section 1.

Pre-crash data and crash data are asynchronous. The sample time accuracy requirement for pre-crash time is -0.1 to 1.0 sec (e.g., T = -1 would need to occur between -1.1 and 0 seconds.)

Accuracy requirement only applies within the range of the physical sensor. If measurements captured by a sensor exceed the design range of the sensor, the reported element shall indicate when the measurement first exceeded the design range of the sensor.

# Comments

A larger recording interval than for light duty EDR is necessary as the event is not necessarily triggered directly by a collision. Therefore, an interval of -10 to 10 sec should be considered.

Suggest removal of engine hours since it is the hours on the powertrain and not the total vehicle hours.

Needs to be split in two elements: "Engine hours, event" and "Engine hours, download" to provide a relative timestamp. See example of "ignition cycle" in UN R160

Suggest base format on PGN 65253, SPN 247 (Engine Total Hours of Operation)

Consider more realistic value

Request to exclude based on anonymity requirement; 'engine hours' would provide the required relative timestamp instead

Request to exclude based on anonymity requirement; 'engine hours' would provide the required relative timestamp instead

For all of these that have details not  yet defined we need to define then we can agree .

wouldn’t you want for all records so: Last Stop,

ABS activation

Automated Emergency Braking

Electronic Stability Control

Road Speed Deceleration

Frontal event

R/O event

For odo should we suggest using  1939 as the element range/res/acc

lacking date/time, the elements Odometer, Ignition Cycle at Event and Ignition Cycle at readout are necessary to tie a data set to the particular event.

Request to add footnote: ‘Shall not contain unique serial numbers or other unique identifiers.’

No proposal on format.

If serial number traceability is integral to Part# - it does not need to be reported.

Request to add footnote: ‘Shall not contain unique serial numbers or other unique identifiers.’

No proposal on format.

Considering privacy complications – decision is whether to delete these data elements

Propose for EU market to combine make/model in one element to record type-variant-version code according to Regulation (EU) 2018/858, Annex I, Part B

Delete make/model and truncated VIN

Rather than make/model have first of VIN w/o sequence number instead of make model in EDR

No proposal on format

Not needed as a mandatory parameter. If required, this data can be pulled from the vehicle.

If this is road speed decel then rename parameter to road speed calibration value.

Range to be discussed so as not to set during normal operation like ABS cycling

Last Stop,

ABS activation

Automated Emergency Braking

Electronic Stability Control

Road Speed Deceleration

Frontal event

R/O event

Request to add footnote: ‘Shall not contain unique serial numbers or other unique identifiers.’

No proposal on format.

You can pull this with the diagnostic tool this is not needed in the EDR .

Propose for EU market to record at least the regulated systems with terminology based on Regulation (EU) 2018/858

This  is not available on the bus necessarily so delete

EC - Suggest exclude both 'ignition cycle' signals because 'engine hours' would provide the required relative timestamp instead

OICA – This parameter is not used today so our recommendation is to leave ign cycle at crash and download out as a mandatory element – Industry practice is to use ODO

Deletion to be confirmed by NL

No proposal on format. Consider basing on PGN 61440, SPN 900 (Retarder Torque Mode)

Need to  define this data element .  Need resolution values is the  J1939 signal  definition appropriate ? this should be recorded for all as well .

All means the Events recorded for are

Last Stop,

ABS activation

Automated Emergency Braking

Electronic Stability Control

Road Speed Deceleration

Frontal event

R/O event

Not sure if this status exists.  Percent value (0-100%) of brake pedal position to be discussed.

Suggest base format on PGN 61444, SPN 513 (Actual Engine - Percent Torque)

How is range -125% to 125%?

Add faulted (note that faulted is now included in latest GRSG rev!!)

Do we need to add off if feature can be turned off?

Same issue as above

These are 1939 signals but should we have them common with R160 or should we keep 1939 as they are already used and defined for HD ?  we think if 1939 has states defined then stay with those states.  should pick minimum states that all ACC systems have.  This should also be recorded for all .

All is : Last Stop,

ABS activation

Automated Emergency Braking

Electronic Stability Control

Road Speed Deceleration

Frontal event

R/O event

Relevant element for general safety research/statistics purposes to identify a potential safe minimum setting

EC - Suggest exclude OICA agrees to exclude

EC - Suggest exclude OICA agrees to exclude

EC - Suggest exclude OICA agrees to exclude

We suggest remove this and the 2 yaw elements  and have stability control engine braking only  with enumerated states for stability/roll intervention

Suggest rename 'rollover protection brake control' to align with SAE standard terminology

OICA – Remove element

OICA – Remove element

Suggest exclude if the states off/faulted of rollover and yaw control are captured in above signals.

Definition needed.  We suggest this be part of stability control enumerated state.  we will work on our suggestion we will use R160 as a starting point.

Suggest rename “crash type” to align with SAE standard terminology.

Need definition of this.  Is this the flag that air bag deployed? If yes then, Enumerated state no event, r/o event , frontal  event .  1939 calls it crash notification suggest we use this name for the data element

Remove side event as this is not a HD feature that we know of

Rather than capturing all this in one signal suggest creating a separate row per pre-tensioner and airbag, compare UN R160

Added this item because VRU System Status was replaced with the alert system. We should capture deployment of passive/secondary safety systems (e.g., deployable hood) nd also active safety systems (warning systems).

we recommend deleting this as VRU not a feature for large trucks   see other note that if this is ped braking include that as an enumerated state for AEB.

Suggest split VRU alert in four signals for easier recording and to replace moving off information system and reversing motion signals further down

Suggest exclude to reduce memory

Agree with EC to delete

See comment above

Suggest exclude to reduce memory

Agree with EC to delete

If you do not have side air bag trigger is there a reason to record this element? Suggest deleting

If you do not have side air bag trigger is there a reason to record this element? Suggest deleting

If no lateral acceleration measurement, then resultant is redundant to longitudinal

If no lateral acceleration measurement, then resultant is redundant to longitudinal

Should remove this element as it is not a parameter of HD systems.

Necessary data element to identify cause of losing control of the car due to external reasons (wind, banking of the road, etc.)

If your system has an angular rate sensor.  we need the same recommendation as pass car for data storage time.

We recommend removal.   This is such low G that it will not provide valuable information for HD

We recommend removal.   This is such low G that it will not provide valuable information for HD

If non integrated / data not available on the vehicle bus, not mandatory .  remove VRU.  Frontal and R/O events recorded for.

I don’t think is for any event you will not make a call on an ABS activation so it is frontal and r/o events only

Record for all triggers. Last Stop,

ABS activation

Automated Emergency Braking

Electronic Stability Control

Road Speed Deceleration

Frontal event

R/O event

Remove rear and mid front data element.

Remove rear and mid front data element.

Suggest replacing with VRU alert signals as suggested above.

Definition needed before OICA can comment

Suggest replacing with VRU alert signals as suggested above.

Is this front or rear  rear pedestrian braking? Definition needed then we can comment.

Recommend removal,  Most of  these system are separate and not integrated and on the vehicle bus .

Value in UN R160 given without unit, su unclear meaning? May need input from accident reconstructionist /industry.

Our recommendation is to remove  all of these CSF/ESF/ACSF elements .  Are these part of R79 and then recorded as part of  DSSAD eventually?     Discussion required on these steering function elements.